Dynamical Systems TIF155/FIM770
Konstantinos Zakkas
Problem Set 2

2.2 Damped pendulum

 ddot θ = -{g over l} sin( θ )- { γ } over {m}dot θ newline ω = dot θ

Now the second order ODE will be written as two first order ODEs

dot θ = ω newline dot ω = - {g over l} sin(θ) - {γ} over {m} ω

Next step is to de-dimensionalise the parameters

θ = θ_0 x newline ω = ω_0 y newline t = t_0 t'

where x, y, t' are the new dimensionless parameters. So if we substitute them we have

θ_0 over t_0 dx over dt = ω_0 y newline ω_0 over t_0 dy over dt = - {g over l} sin(θ_0 x) - γ over m ω_0 y

thus if we choose t_0 = sqrt( l over g ) in order for t_0 to have s as its unit, since the unit for g is m over s^2 and for l is m we get

dx over dt = sqrt( l over g ) ω_0 over θ_0 y
dy over dt = -{ g over l } sqrt( l over g ) {sin( θ_0 x )} over ω_0 - γ over m sqrt( l over g ) y

and it was given that

dx over dt = y newline dy over dt = -sin( x) - σ y

so comparing the our system with the one we want to have we get

sqrt( l over g ) ω_0 over θ_0 = 1 newline σ = γ over m sqrt( l over g ) newline θ_0 = 1

and for θ_0 = 1 we have

ω_0 = sqrt( g over l )